Vanellus C6 Extra

Long Drain SHPD Diesel Engine Oil

_____________________________________________________________________________

Applications

| Vanellus C6 Extra is a long drain Super High Performance Diesel (SHPD) multigrade engine oil, designed for use in turbo-charged diesel engines operating under demanding conditions. It is formulated using high quality conventional base oils in combination with high performance additives to provide good protection against wear and deposit accumulation. | Vanellus C6 Extra is designed for longer oil drain intervals in accordance with the engine manufacturers recommendations. Vanellus C6 Extra is also suitable for use in normally aspirated diesel engines in commercial vehicles. |
| --- | --- |

_____________________________________________________________________________

Main Benefits

| • High levels of engine cleanliness and wear protection in turbo and non-turbo charged diesel engines • Good protection against bore polishing • Good high temperature performance against deposit and lacquer formation | • Longer engine oil drain intervals in accordance with the engine manufacturers recommendations. • All round protection will extend your engine life and decrease expensive downtime |
| --- | --- |

_____________________________________________________________________________

Specifications

| Vanellus C6 Extra exceeds the performance requirements of: • API CH-4 • ACEA E3, E5, B3, B4 • Mercedes-Benz Sheet 228.3 • MAN M3275 | • Renault VI RLD • Volvo VDS-2 • Cummins CES 20072 |
| --- | --- |

_____________________________________________________________________________

Storage

| All packages should be stored under cover. Where outside storage is unavoidable drums should be laid horizontally to avoid the possible ingress of water and | the obliteration of drum markings. Products should not be stored above 60°C, exposed to hot sun or freezing conditions. |
| --- | --- |

_____________________________________________________________________________

Health, Safety and Environment

| Health, safety and environmental information is provided for this product in the Materials Safety Data Sheet. This gives details of potential hazards, precautions and First Aid measures, together with environmental effects and disposal of used products. | BP p.l.c. or its subsidiaries will not accept liability if the product is used other than in the manner or with the precautions or for the purpose/s specified. Before the product is used other than as directed, advice should be obtained from the local BP office. |
| --- | --- |

_____________________________________________________________________________

_____________________________________________________________________

Vanellus C6 Extra

Long Drain SHPD Diesel Engine Oil

_____________________________________________________________________________

Typical Characteristics

_____________________________________________________________________________

|  | Test Methods | Units | Grade : |
| --- | --- | --- | --- |

_____________________________________________________________________________

_____________________________________________________________________________

|  |  |  | SAE 15W-40 |
| --- | --- | --- | --- |
| Density at 15 °C | ASTM D1298 | kg / m³ | 885 |
| Flash Point (COC) | ASTM D92 | °C | 210 |
| Kinematic Viscosity at 40°C | ASTM D445 | mm² / s | 119.5 |
| Kinematic Viscosity at 100°C | ASTM D445 | mm² / s | 15.9 |
| Viscosity Index | ASTM D2270 | - | 142 |
| Pour Point | ASTM D97 | °C | -25 |
| Total Base Number | ASTM D2896 | mgKOH/g | 11.8 |

_____________________________________________________________________________

The above figures are typical of those obtained with normal production tolerance and do not constitute a specification.

| This Data Sheet and information it contains is considered to be accurate at the date of printing. No warranty or representation, expressed or implied, is made as to the accuracy or completeness of the data and information contained in this publication. | The Seller shall not be responsible for any loss or damage resulting from any hazards or risks identified in the data sheet and which are associated with petroleum products concerned (provided that this disclaimer shall not affect any statutory rights of the Buyer of the petroleum products concerned). |
| --- | --- |
| It is the User's obligation to evaluate and use products safely and within the scope advised in the data sheet and to comply with all applicable laws and regulations. No statement made in this publication shall be construed as a permission, recommendation or authorisation given or implied to practice any patented invention without a valid licence. |  |

_____________________________________________________________________________